## Slide 1: Reduced Instruction Set Computers
YWCC-307-103

## Slide 2: What is Reduced Instruction Set Computers and It’s History
RISC, or Reduced Instruction Set Computer is a type of microprocessor architecture that utilizes a small, highly-optimized set of instructions, rather than a more specialized set of instructions often found in other types of architectures.
The first RISC projects came from IBM, Stanford, and UC-Berkeley in the late 70s and early 80s. The IBM 801, Stanford MIPS, and Berkeley RISC 1 and 2 were all designed with a similar philosophy which has become known as RISC.

## Slide 3: characteristic of most RISC processors
Simplified instructions, taking 1 clock cycle
Large no. Of general purpose registers.
Circuit is much simpler
Fast to decode
Fast to execute
Pipelining- fetching of next instruction while previous instruction executes.

## Slide 4: Complex Instruction Vs. Reduced Instruction set Computers
CISC
Emphasis on Hardware
Includes multi-clock complex instructions
Many operations in single instruction
Small codes sizes but complicated
Instruction size varies in different instructions.
RISC
Emphasis on software
Single-clock, reduced instruction only
One instruction one operation.
Larger code size but simple
Same instruction size in every instructions

## Slide 5: RISC Application
LOW END & MOBILE SYSTEM
ARM Architecture in Android devices, Apple iPhone, and Nintendo GBA
MIPS Line in PlayStation, Nintendo 64
Atmel AVR in Xbox controllers to BMW cars
HIGH END & Supercomputing
MIPS in routers
IBM’s Power Architecture in many IBM supercomputers and workstations
Alpha in single-board computers, servers & Supercomputer

## Slide 6: Reference
https://cs.stanford.edu/people/eroberts/courses/soco/projects/risc/whatis/index.html
https://www.microcontrollertips.com/risc-vs-cisc-architectures-one-better/
http://embeddedcraft.org